## Slide 1
DREAMER: a new reconfigurable logic platform
  New point in the space between programmability and efficiency
  Instead of array of bits, use parallel array of simple processors
    Each tile executes a portion of design’s hardware graph (right)
  Supporting tools to map RTL to array
    Compiles in seconds, not hours
  Integrated debugging support
    Probe state without recompiling
  Overall, faster design iteration time
Fast reconfigurable logic for emulation
Dreamer
Palmer Dabbelt, Richard Lin, Albert Magyar
FPGA area optimization
Pipelining for faster clock speeds and realistic SRAM data memory
Automatic instruction set generation and specialization
DSP optimization
Efficiently handling fine-grained (bit-width) operations
Background
The Design-Test-Execute Loop
Design – test – execute: current iterative method for hardware design
Iron Law of Emulation
Time to simulate a design depends on tools and cycles
  Software: fast compile times, but slow emulation for complex designs or long simulations
  FPGA: high compile overhead, suitable for complex designs
  ASIC: if you have lots of time and money to burn…
Practically, FPGA emulation is the fastest tool for emulation … but still isn’t ideal:
  Inefficient support for word-wide operations (natively bit-wide)
  Logic synthesis and mapping takes a long time
  … and must be done after any change in the design
  … even if all you want to do is add a logic probe
Generalizing from emulation, array can be used as a general dataflow style machine
  Can even be programmed in Chisel
  … or parallel assembly, if you’re feeling adventurous
  Edge ports can be connected to any ready-valid interface:
    GPIO, DRAM, or coprocessor data movement
Possible applications
  General-purpose reconfigurable logic coprocessor
  DSP filtering, or really anything dataflow-parallel
FPGA
(Zedboard with Xilinx Zynq)
  See our pretty demos!
16 tiles in a 4 x 4 array
Clock: 40 MHz
ASIC
(TSMC 45nm process)
0.9 ns clock (1.1 GHz)
63,442 µm2 per tile (1,576 tiles in 100mm2, 4,728 tiles in 300mm2)
Specs:
1024 x 32 data memory
1024 x 32 code memory
32 x 32 register file
In the big picture:
Architecture
Dataflow Machine
Hardware Implementation
Future Work
The Array
Massively parallel array of simple compute tiles
  Cores connected in a nearest-neighbor network
  Each connection is a 2-element buffer (reduce deadlocks)
  Ready-valid interlocked ports (avoid explicit no-ops)
  Additionally, all tiles’ host interfaces connected in a scan chain (for debugging and control)
  Edge ports can be mapped to external data
Statically scheduled computation and communication
  Simple hardware architecture, push complexity to tools
  All inter-tile data movement explicit (one tile at a time)
The Tile
Simple compute cores
  A mini computer – datapath, registers, memory, and code
  Reduced ISA specialized for simulation, containing:
    your standard arithmetic / bitwise-logical operations
    emulation-specific instructions like mux
  No branching – simple emulation loop
Dedicated host interface
  Process host command packets in-place, then shift response to next tile in chain
  Arbitrary peek/poke access into all state elements
  Control tile execution
Overview
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about