## Slide 1
DREAMER Motivation
… but FPGA emulation is not ideal
  Inefficient support for word-wide operations (natively bit-wide)
  Logic synthesis and mapping takes a long time
  … and must be done after any change in the design
  … even if all you want to do is add a logic probe
DREAMER: a new reconfigurable logic platform
  New point in the space between programmability and efficiency
  Instead of array of bits, use parallel array of simple processors
    Each tile executes a portion of design’s hardware graph (right)
  Supporting tools to map RTL to array
    Compiles in seconds, not hours
  Integrated debugging support
    Probe state without recompiling
  Overall, faster design iteration time
Fast reconfigurable logic for emulation
Dreamer
Architecture
Palmer Dabbelt, Richard Lin, Albert Magyar
The Array
Massively parallel array of simple compute tiles
  Cores connected in a nearest-neighbor network
  Each connection is a 2-element buffer (reduce deadlocks)
  Ready-valid interlocked ports (avoid explicit no-ops)
  Additionally, all tiles’ host interfaces connected in a scan chain (for debugging and control)
Statically scheduled computation and communication
  Simple hardware architecture, push complexity to tools
  All inter-tile data movement explicit (one tile at a time)
The Tile
Simple compute cores
  A mini computer – datapath, registers, memory, and code
  Reduced ISA specialized for simulation, containing:
    your standard arithmetic / bitwise-logical operations
    emulation-specific instructions like mux
  No branching – simple emulation loop
Dedicated host interface
  Process host command packets in-place, shift response to next tile in chain
  Arbitrary peek/poke access into all state elements
  Control tile execution
Overview and Motivation
The Design-Test-Execute Loop
Design – test – execute: current iterative method for hardware design
Dataflow Machine
Hardware Implementation
???
Iron Law of Emulation
Time to simulate a design depends on tools and cycles
  Software: fast compile times, but slow emulation for complex designs or long simulations
  FPGA: high compile overhead, suitable for complex designs
  ASIC: if you have lots of time and money to burn…
Practically, FPGA emulation is the fastest tool for emulation
Generalizing from emulation, array can be used as a general dataflow style machine
  Can even be programmed in Chisel
  … or parallel assembly, if you feel more adventurous
  Edge ports can be connected to any ready-valid interface:
    GPIO, DRAM, or coprocessor data movement
Possible applications
  General reconfigurable logic coprocessor
  DSP filtering, or really anything dataflow-parallel
FPGA
(Zedboard with Xilinx Zynq)
  See the pretty demos!
16 tiles in a 4 x 4 array
Clock: 40 MHz
ASIC
(TSMC 45nm process)
0.9 ns clock (1.1 GHz)
63,442 µm2 per tile (1,576 tiles in 100mm2, 4,728 tiles in 300mm2)
Specs:
1024 x 32 data memory
1024 x 32 code memory
32 x 32 register file
In the big picture:
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about